©          Troubleshooting Guidelines

Troubleshooting for faulty or defective sets will

be conducted according to the following procedures.

1. Visual inspection

Check the condition of install, switch of power supply, joining of connectors, break or bend of PCB, bad soldering or Short of components and problem of part ,etc.

2. Power Test

| Check power supply(SMPS) | Concerned part(SMPS) |
| --- | --- |
| Symptom:The system does not work and there is no Action in front display after power on. |
| In this case, check the connection of power supply connector whether it is connected to the board correctly or not. Turn on the power switch and check the output power source as follows: (1) +12V Check the power at BC204 (2) +5V Check the power at L53 (3) +3.3V Check the power at L56 (4) +1.1V Check the power at L55 (5) +1.5V Check the power at U59 The normal range of reference values are as follows: Parameter Min Typ Max Unit (1)+12V 12 12.16 12.3 V (2)+5V 5 5.1 5.5 V (3)+3.3V 3.2 3.3 3.5 V (4)+1.1V 1.0 1.1 1.3 V (5)+1.5V 1.4 1.5 1.6 V Management: Check power supply connections lf the connection is valid and there is no power then disassemble the connector and check the SMPS output device only. lf the power SMPS supply output is normal, then there is probably a short circuit between the CPU board and GND; therefore, inspect the CPU board. However, if the SMPS output is abnormal, then replace the SMPS and re-inspect the system. |

3. System Test

| Check main system clock | Concerned Part:X-tal(X1) |
| --- | --- |
| Symptom: The system does not boot or intermittently acting after power on. |
| Basically, the system uses 27MHz Crystal clock. CPU(U18) gets 27.000MHz system clock, and then generates other clocks for system use. If this clock is abnormal, the system dose not work correctly. To verify this clock, check the clock signal at both ends of Crystal. Management: If clock shape is unlike as show above, it is possible that Crystal(X1) is damaged. Check components R89、R90、BC99、BC101 whether it is bad soldering or damaged. If you cannot find any problem,replacement of Crystal is required. |
| Test for boot sequence | Concerned Part: CPU(U18),Flash-Room(U38) |
| Symptom: The system does not boot or intermittently acting after power on. |
| Basically, system starts boot sequence after that power is on . If power supply of a set is normal and the set does not start boot sequence, it is possible that signals between CPU and Flash-Rom are abnormal. Check the SPI-BUS signal of Flash-Rom. |
| DDR test | Concerned Part :DDR(U19) |
| Symptom：Screen show entirely green or seriously broken. |
| Basically, cpu uses DDR as MPEG decoding memory. Therefore, abnormal working of DDR causes broken video screen or wholly green. In this case, check the DDR control signal as below. Management: The frequency of DDR clock signal is about 400MHz. If the above signal is ok, examine the signal for all address and data pins. If you can not find any problem with this test, replacing chip should be the last option. |

4 .MPEG and A/V Test

| MPEG decoder test | Concerned part:MPEG Decoder (U18) |
| --- | --- |
| Symptom: System is normal, but video signal does not appear. |
| MPEG decoder has video outputs CVBS. The picture shown down below is the output pattern. The waveform is measured in standard color bar signal. Management: If there is no signal at these check points,resoldering of the MPEG decoder is required.If there is no video signal at output port but MPEG decoder outputs are normal, trace the circuit related RCA and check the waves. If you can not solve the problem with these method, it is possible that replace the MPEG decoder(U18). |
| Audio and Video Test | Concerned Part: U18 |
| Symptom: Audio or Video signal is not generating |
| If the system is normal,but audio or video signal does not appear , check analog audio output of U18or check digital video output of U18， Refer to below waveform diagrams. If analog audio signal is normal, trace the route of analog audio signal from U18 output to AV jack. If digital video signal is normal,trace the route of digital video signal from U18output to AV jack.Or CPU(U18) can be replaced. The waveform is measured in standard color bar signal. |

5. TUNER Test

| Check power and control signal on tuner | Concerned part: Tuner(UT05)、DEMO(U8) |
| --- | --- |
| Symptom: You can not scan channels and signal strength bar is very low. Channel is locked,but no signal displayed. |
| Management: First of all,make sure antenna cable is connected correctly.If that is correct,check below points of LNB power control part. 13V(vertical) or 18V(horizontal) Check D33 3.3V Check Pin 2 of UT05 If all of these powers are correct and the set still has problem，check all of signals associated with tuner(UT05). |

6. Maintenance Problem Point

(1) Not starting up, no response Cause analysis: The input capacitance is bad(BC204) Maintenance methods: Using a multimeter to test the BC204，if it is short，replace the capcitance.

(2) Not starting up, only display LED lamp Cause analysis: The Power IC is bad（example U61、U62）; The DDR parameter is wrong, need to update Bootloader 2. Use oscilloscope measurement 27M crystal oscillator frequency whether it is 27M; 3. The CPU is bad. Maintenance methods: 1. Using a multimeter to test the Power（3.3V, 1.2V, 1.5V, 5V），if the value not normal，replace the corresponding IC. 2. Power on and power off more than once, depends on the former control board whether can show BOOT, if show, that means is Bootloader problem, which will be updated software name to ROM. Bin, insert USB, boot hold panel standby key began to update; 3. Test 27M crystal oscillator frequency is not normal, the need to change the crystal oscillator; 4. Using a multimeter to test CPU power supply normal, 27M crystal oscillator is normal, software Bootloader normal, with resistance file test DDR on impedance normal, replace the CPU.

(3) Not starting up, BOOT display Cause analysis: DDR parameter is wrong, need to update Bootloader Maintenance methods: Should copy ROM. Bin file in the root directory of USB device,insert USB, boot hold panel standby button to start updata.

(4) Display Signature fail Cause analysis: No serial number Maintenance methods: Use the SERIAL_TOOL to write the serial number.

(5) There are signal quality, no program image Cause analysis: 1.The LNB power not normal 3. The demo U8 dry solder(production process problems); 4. Demo U8 is bad (electrostatic damage). Maintenance methods: Use the oscilloscope test the D33(D7). The normal waveform as the image below(with 75Ω load) Use the multimeter to test the voltage of the D33(13V/18V) If the LNB power not normal, 2.With maintenance visual method to see demo chip pin is cold solder. 3. Using a multimeter to measuring demo of the power supply voltage of 3.3 V, 1.2 V, visual inspection chip is cold solder, change Test.

(6) Not starting up or Picture pause, chip EPAD cold solder Cause analysis: 1. Play more than 30 minutes after the crash 2.Because of the production process problems, transportation vibration lead to CPU EPAD bad contact GND, SHPE1512A chip EPAD bottom must be ground, or it will cause the machine can't start. Maintenance methods: 1. In the change before the CPU, it is necessary to heating the chip bottom, after heating the fault is still to exist then replace CPU. 2. Methods: using soldering iron heating the PCB board at the back of the joint area.

# Text boxes

27.000MHz  Clock

Check Point BC99 or BC101

SPISCK signal

CheckPoint:Pin6 of U38

SPIMOSI signal

Check Point:Pin5 of U38

DDR Clock: 397.5MHZ

Check Point: R209 or R210

CVBS：Check Point D27

AUD_R

Check Point : D28

PIN 1: LNB

PIN 2: 3.3V

PIN 3: AGC

PIN 4: IP

PIN 5: IN

PIN 6: QP-

PIN 7: QN-

PIN 8: SDA

PIN 9: SCL

PIN 10: CLK_OUT

SCL

Check Point Pin 9 of UT05 or TR48

SCL: Check PIN9

SDA: Check PIN8